## Slide 1: CIS 525 – Introduction to Networking Final Exam Review: Everything from the Exam I and II review slides, plus the following…
Eugene Vasserman

## Slide 2: Available Bandwidth
Knee load: critical bandwidth when latency increases significantly
Wanted to keep the load around the knee
Assume that timeout mechanism provides feedback about reaching the knee load

## Slide 3: AIMD with Congestion Avoidance
congestion
avoidance
additive
increase

## Slide 4: TCP Packet Pacing
Congestion window helps to “pace” the transmission of data packets
In steady state, a packet is sent when an ACK is received
  Data transmission remains smooth, once it is smooth
  Self-clocking behavior
Pr
Pb
Ar
Ab
Receiver
Sender
As

## Slide 5: Silly Window Syndrome
Interaction:
  After the receiving application reads an octet from a full buffer, one octet of space is available
  Then, TCP generates an ACK to advertise an “available” window size of 1 octet
  The sending TCP implementation composes a segment containing 1 octet of data
This interaction (called the Silly Window Syndrome) results in a steady state in which TCP sends a separate segment for each octet of data
Each ACK advertises a small amount of space available, and each segment carries a small amount of data

## Slide 6: Avoiding Silly Window Syndrome
Reciever-Side Avoidance:
  Before sending an advertisement after advertising a zero window, wait for space to become available that is 50% of the total buffer size or equal to a maximum sized segment
Sender-Side Avoidance (Nagle’s Algorithm):
  When previous data has not been acknowledged, do not send additional data until a maximum-sized segment is full
  When an ACK arrives, send all data that has accumulated, even if the segment is not full

## Slide 7: Slow Start Packet Pacing
How do we get this clocking behavior to start?
  Initialize cwnd = 1 (one MSS)
  Upon receipt of every ACK, cwnd = cwnd + 1
Implications
  Window actually increases to W in RTT * log2(W)
  Can overshoot window and cause packet loss

## Slide 8: Return to Slow Start
If packet is lost, we lose our self-clocking as well
  Need to implement slow-start and congestion avoidance together
When timeout occurs set ssthresh to W/2
  If cwnd < ssthresh, use slow start
  Else use congestion avoidance

## Slide 9: Fast Retransmit
What are duplicate ACKs (dupACKs)?
  Repeated ACKs for the same sequence
When can duplicate ACKs occur?
  Loss
  Packet re-ordering
  Window update – advertisement of new flow control window
Assume re-ordering is infrequent and not of large magnitude
  Use receipt of 3 or more duplicate ACKs as indication of loss
  Don’t wait for timeout to retransmit packet

## Slide 10: Delayed ACKS
Problem:
  In request/response programs, you send separate ACK and Data packets for each transaction
Solution:
  Don’t ACK data immediately
  Wait 200ms
  Must ACK at least every other packet – why?
  Must not delay duplicate ACKs – why?
Notes: Wait must be less than 500ms – why?

## Slide 11: Delayed ACK Impact
TCP congestion control triggered by ACKs
  If receive half as many ACKs  window grows half as fast
Slow start with window = 1
  Will trigger delayed ACK timer
  First exchange will take at least 200ms
  Start with > 1 initial window
    Bug in BSD, now a “feature”/standard

## Slide 12: Round Trip Time Estimation
Wait at least one RTT before retransmitting
Importance of accurate RTT estimators:
  Low RTT estimate
    Unnecessary retransmissions
  High RTT estimate
    Poor throughput
RTT estimator must adapt to change in RTT
  But not too fast, or too slow!
  “Conservation of packets” principle – never more than a window worth of packets in flight

## Slide 13: Timestamp Extension
Used to improve timeout mechanism by more accurate measurement of RTT
When sending a packet, insert current timestamp into option
  4 bytes for timestamp, 4 bytes for echo
Receiver echoes timestamp in ACK
  Actually will echo whatever is in timestamp
Removes retransmission ambiguity
  Can get RTT sample on any packet

## Slide 14: Sliding Window Revisited
Sending Side
LastByteAcked <= LastByteSent
LastByteSent <= LastByteWritten
Buffer bytes between LastByteAcked and LastByteWritten
Receiving Side
LastByteRead < NextByteExpected
NextByteExpected <= LastByteRcvd +1
Buffer bytes between NextByteRead and LastByteRcvd
Sending application
LastByteWritten
TCP
LastByteSent
LastByteAcked
Receiving application
LastByteRead
TCP
LastByteRcvd
NextByteExpected

## Slide 15: TCP Sawtooth Behavior
Time
Congestion
Window
Initial
Slow start
Fast
Retransmit
and Recovery
Slowstart
to pace
packets
Timeouts
may still
occur

## Slide 16: Session Layer
“Value-added” services built on top of transport layer
    Rollback / recovery
    Remote procedure calls (RPC)
  Three phases:
    Establishment
    Use
    Release
Presentation Layer Protocols
  ASN.1

## Slide 17: Rollback / Recovery
Checkpoints can be used to mark known consistent states
When a failure occurs, the session can be rolled back to the previous checkpoint
Example: advanced file transfer protocols use rollback recovery

## Slide 18: Presentation Layer
Preserves meaning of transmitted information
  See how this fits in with RPC?
Three major issues:
  Representation
  Compression
  Encryption (Chapter 8)

## Slide 19: Box Notation vs. Type-Length-Value
Box notation
  Intuitive way of describing a data format
  Field types/encoding specified separately
  Limitations: no variable-length fields
Type-Length-Value (TLV), or tabular/tuple
  Representation of variable-size or optional message fields
  Can be parsed without understanding the meaning of the field

## Slide 20: ASCII Box Notation for TCP Header [RFC 793]

## Slide 21: Example: TCP Header Options

## Slide 22: Canonical Intermediate Forms
Tabular and Box format
Type-Length-Value (TLV)
  Example: ASN.1 – Abstract Syntax Notation One
  Tagged message type: <type, length, value>
  Support compound (seq) types:
  <type(seq),length,type,length,value,type,length,value>
Fixed format
  Example: XDR – eXternal Data Representation
  Defines standard format for basic data types
  Untagged – must define XDR stream, and encode or decode
  See Ex17.c

## Slide 23: Encoding
ASN.1 doesn’t determine transfer syntax
Standardized encoding rules:
  Basic encoding rules (BER) [X.690]
  Canonical and Distinguished encoding rules (CER, DER)
  Packed encoding rules (PER) [X.691]
  XML encoding rules (XER) [X.693]
  Specification of specialized encoding rules: Encoding control notation (ECN) [X.692]

## Slide 24: Basic Encoding Rules (BER)
Rules for encoding abstract into concrete data
Encoding in TLV style (tag-length-value)
TLVs can be nested, i.e. the value can contain a sequence of TLVs

## Slide 25: BER vs. Other Encoding Rules
Shortcomings of BER:
  Lengthy: type and length fields are always octets, e.g. a boolean value requires 3 octets (24 bits)
  Encoding rules with some degrees of freedom (e.g. different ways of cascading TLVs)
CER/DER (Canonical and Distinguished Encoding Rules)
  Restrictions on BER: only one possible encoding (injectivity; used in security protocols, e.g. exchange of certificates)
PER (Packed Encoding Rules)
  Size reduction by giving up the TLV format

## Slide 26: Packed Encoding Rules
PER format: [P][L][V] instead of TLV:
  Optional preamble,
  Optional length,
  Optional value
Series of bits instead of octets
Tags are not encoded
Preambles are used for choices
Length is only encoded when necessary (e.g. no type size limitation by the ASN.1 specification)
Optional components of a sequence or set is indicated in a bitmap preceding the value encoding

## Slide 27: BER vs. PER Example: BER

## Slide 28: BER vs. PER Example: PER
PER can reduce the overall length of the encoding, but it’s not as extensible
101 1 01 1 0

## Slide 29: XML Encoding Rules (XER)
Delimit ASN.1 values with XML markups

## Slide 30: Simple Network Management Protocol (SNMP)
UDP/IP network management protocol
Defines communication between manager and agent
  Message formats
  Interpretation of messages
  Data representation (using ASN.1)

## Slide 31: Fetch-Store Paradigm
Manager-agent interaction based on fetch-store paradigm and trap paradigm
  Fetch retrieves a value from the agent
  Store changes a value on the agent
  Trap send a value from agent to manager
Fetch: monitor internal data values and data structures
Store: modify and control data values and data structures; also control behavior
Trap: report alarm conditions

## Slide 32: SNMP Operations
Get (fetch) retrieves value of object
Set (store) stores new values into object
Get-next retrieves next object (for scanning, or “walking”)
Trap for agent to send alarm to manager

## Slide 33: SNMP Message Format

## Slide 34: SNMP Example “Decoded”
viper% snmpget -v1 -d -c public 129.130.10.39 ip.ipInReceives.0
30 29 02 01 00 04 06 70 75 62 6C 69 63 A0 1C 02
04 2C 79 D1 3C 02 01 00 02 01 00 30 0E 30 0C 06
08 2B 06 01 02 01 04 03 00 05 00
30 29 = sequence of 41 bytes
02 01 00 = version (00 + 1) = version 1
04 06 70 75 62 6C 69 63 = community string (“public”)
A0 1C = PDU type = “GET”, total request length 28 bytes
02 04 2C 79 D1 3C = REQUEST ID
02 01 00 = ERROR STATUS
02 01 00 = ERROR INDEX
30 0E = sequence of length 14 bytes containing request
30 0C = sequence of length 12 bytes containing OID
06 08 2B 06 01 02 01 04 03 00 = 1.3.6.1.2.1.4.3.0
05 00 = NULL String of length 0 (END OF STRING)

## Slide 35: Domain Name System (DNS)
Translates human-readable domain names to IP addresses
“Simple” query-response over UDP
  Compare to Address Resolution Protocol (ARP)
Security concerns (poisoning, etc.)
  DNSSEC
  Partial/temporary fixes
May someday replace certificate infrastructure (HTTPS (TLS))

## Slide 36: Security Basics
“Secure against what?”
  Threat/attacker model, players and resources
The only thing secret about a secure system should be the “secret key”
–Kerckhoffs’ principle
“The enemy knows the system”
–Shannon’s maxim
Notes: No security through obscurity, although perhaps security through obfuscation
Secure hardware
From “Satan’s computer”: “a computer which gives answers which are subtly and maliciously wrong at the most inconvenient possible moment” – safety vs. security

## Slide 37: Safety vs. Security
Think like an adversary!
Random → malicious faults
Engineering for security:
“What’s the worst that can happen?”
Assume it will…
Always, always, ALWAYS state your assumptions!

## Slide 38: Tools: Encryption
Basic idea: someone seeing ciphertext learns nothing about plaintext without correct key
With or without authentication
Symmetric – based on tests/best guess
  e.g. AES (block cipher)
Asymmetric – based on math assumptions
  e.g. RSA
Notes: Start with substitution cipher… Why not?
Difference in assumptions/security between symmetric and asymmetric
Symmetric is ~10x faster

## Slide 39: Authenticity and Integrity
Basic ideas:
  Authenticity: the message was produced by a specific known subject
Authentication ≠ integrity
  Integrity: the message has not been altered between source and destination
Messages without integrity protection vulnerable to chosen ciphertext attack
Notes: Why do we need e.g. integrity when encrypting?
What doesn’t this say? Time? One-time [unconditional] authentication codes

## Slide 40: Key Agreement: Person-in-the-middle
Alice
Bob
Alice
Private
NOT Authenticated
Bob
?

## Slide 41: Key Agreement: Person-in-the-middle
Muahaha!
Alice
Bob
Alice?
NOT Private
NOT Authenticated
Bob

## Slide 42: Tools: Authentication
Symmetric (shared key)
Asymmetric
  Trusted third party vs. trust-on-first-use
    TLS (was SSL) and SSH
Why is asymmetric crypto authenticated now, but not a moment ago?
Symmetric is deniable
SSH, TLS, VPN – which is asymmetric?
Notes: Authentication provides what? Authenticity, integrity (signatures).
Any MAC; RSA, DSA
Replay attacks!

## Slide 43: Certificates (TLS)
Alice
Bob
Alice!
Private
Authenticated
Bob
CRAP!

## Slide 44: TLS (was SSL/TLS)
How do we know a website is “genuine”?
We trust a third party
Not:
  “This is mybank.com”
More like:
  “Trusted third party says ‘This is mybank.com’”
What if we swap “trusted” parties?
Trusted vs. trustworthy

## Slide 45: Chain of Trust
User A says:
  I want access to resource R
  Kerberos server, authenticate me!
R does not know if A has rights to access R
Kerberos server:
  Checks if A is who she says she is
  Checks if A is authorized for access to R
R trusts Kerberos server but not A

## Slide 46: Final Exam
Final exam on Tuesday December 11th at 4:10 pm
(same room as class)